## Slide 1
TEAM NAME / LOGO
TECHNICAL APPROACH
SMART INDIA HACKATHON 2026
PS 26123 · ROBOTON
SIH
LOGO
AMR Sensors
[Pose · Proximity]
Operator Order
[Order Gateway]
Warehouse Map
[Graph JSON]
Peer-to-Peer Mesh
[ESP-NOW · 250 B]
Peer State
[INTENT @ 5 Hz]
ON-BOARD EVERY AMR · NO CENTRAL PLANNER
Task Announce
Receiver
Distributed
Auction
Time-Window
A* Planner
Route Reservation
[PATH broadcast]
Precedence
Executor
Self-Healing
[loss · dropouts]
Right of way is decided by booking order, never by the clock. The rule is deterministic, so two robots can never both believe they have it.
Task Delivered
[COMPLETE]
Telemetry
[WebSocket]
Update
Dashboard
Warehouse
Maps
Peer Plan
Table
Event &
Metrics Log
Operator Views (read-only)
Live Fleet
Floor
A/B Benchmark
Panel
Order Entry
Page
Webots 3D
View
TECH STACK
EDGE ROBOT LOGIC
Python 3.11
ESP32 · ESP-NOW
GATEWAY & DASHBOARD
FastAPI
WebSockets
JavaScript
HTML5
SIMULATION & VERIFICATION
Webots 3D
pytest
Git
CORE ALGORITHMS
Sealed-bid reverse auction
Free-time-window A*
Precedence execution (ADG)
Well-formed Kiva-style maps